## Slide 1
Autonomous Aerial Vehicle
Oct. 13 - 2020 | Team 10
Alex Magyari – Team LEAD
Leslie Nix | Ai Nguyen | Sang Nguyen
Project Manager: Dr. Shan

## Slide 2
We seek to provide a transportation system for an air quality sensor that has been developed by Dr. Shan’s research team.
Our overall goal is to solve the problem of determining harmful, aerial byproducts from various sources, such as chemical fires, explosions, and factories.
Purpose
Notes: 1:00

## Slide 3: Background

## Slide 4
Many Potential Customers:
  Specifically designed for Dr. Shan's research team
  Environmental Protection Agency (EPA)
  Investigative government agencies
  Local government
  Private sector members
User Analysis
Notes: 1:45

## Slide 5
Overview Diagram
Notes: 4:00

## Slide 6: Goal Analysis
Receive GPS coordinates via mobile app
Follow path within 3 [m] margin of error
Forward flight speed of 2-4 [m/sec]
Return to starting point after completing flight

## Slide 7: Constraints
Constraint | Limiting Factors
Flight Time | Battery Life Drone Speed
GPS Accuracy | Weather Distance to satellite
Budget | Sponsor Donations Department Contribution
Time to Prototype | CoVid-19 Parts ordering

## Slide 8: Key Specifications
  Maximum Distance: ~4 miles round trip*
  Maximum Battery Life: 16.5 [min] *
  App Controlled: Yes
  On-board GPS: Yes
  On-board BlueTooth: Yes
  Weight (No load): 3.4 [lbs]
  Single or General Purpose: Single Purpose
* Calculated with a 14.8 [V], 4 cell battery, a net weight (with load) of 4.4 [lbs], and a maximum battery discharge of 90%.

## Slide 9: More Specifications
  Device Compatibility: Apple/Android/Google Mobile Devices
  Interchangeable Battery: Yes
  Camera: No
  Flight:
    Autonomous Mode Only via Waypoint Navigation
    Automatic Flight Stabilization
    Automatic Landing
    Adjustable Flight Path and Hover Times

## Slide 10: Schedule

## Slide 11: Application Programming Schedule
Legend
Completed
Progress Since Last Report
Still to be Completed

## Slide 12: Application Controller Subtasks
SUB-TASK | ACCOMPLISHEMENTS | ROADBLOCKS
UI Design | Previously Completed | 
Ionic Installation | Previously Completed | 
Program Interface | Previously Completed | 
BLE-Programming |  | Waiting on BLE from FCU
Application debugging | Thoroughly tested multiple use cases | 

## Slide 13: Quadcopter Construction Schedule
Legend
Completed
Progress Since Last Report
Still to be Completed

## Slide 14: Construction Subtasks
SUB-TASK | ACCOMPLISHEMENTS | ROADBLOCKS
Order parts | All parts received | 
Assemble body | Body assembled | 
Solder Wiring | All components connected, wrapped | Inappropriate ESC firmware – purchased new ESCs
Test Power, Measure Thrust | Completed sweep of motor function with oscilloscope input All motors operating independently | Battery failures – purchased new batteries

## Slide 15: Flight Control Unit Programming Schedule
Legend
Completed
Progress Since Last Report
Still to be Completed

## Slide 16: Flight Controller Subtasks
SUB-TASK | ACCOMPLISHEMENTS | ROADBLOCKS
Install Free RTOS | Previously Completed | 
Program Flight Control System | Installed I2C for peripherals Installed UART for PC debugging | 
Program Motor Control Methods | Programmed PWM signal | 
Implement GPS Communication | Programmed NMEA decoder Programmed GPS input signal | 
Implement BLE Communication | Established the connections Send and Receive signals | Lack of knowledge and documentations about BLE.
Implement Waypoint Navigation | Constructed the waypoint navigation method | 
Perform Flight Test |  | Wait for drone built.

## Slide 17: Test Plan
Drone’s Physical Test | Power Consumption | 
 | Motor Thrust | 
Module Test | Bluetooth Module | Connection Data Transfer
 | GPS Module | Connection Coordinate Reading
Flight Test | Flight Controller | Take Off Landing Move Forward/Backward Turning
 | Speed Test | Max Speed Stability
 | Waypoint Navigation | Approach Waypoint Returning to User
Application Test | Functionalities | Bluetooth Connection GPS Coordinates/Data Transmission Google Map Tracking

## Slide 18: Total Budget

## Slide 19: Standards

## Slide 20: Government Drone Standards
  Weight: 55 lbs (25kg)
  Groundspeed: 100 mph (87 knots)
  Altitude: 400 feet AGL
  Minimum weather visibility: 3 miles
  Schedule: 30 minutes before official sunrise to 30 minutes after official sunset.

## Slide 21: Retail Drone Standards
Standard Flight Time: 15 minutes
Standard Control Method: RC Controller
Typical Features:
  Camera
  Interchangeable Batteries
  Possible app interaction
  Flight stabilization
  Auto-Landing Feature

## Slide 22: Risk Management
Probability | 5 |  |  |  |  | 
 | 4 |  |  |  |  | 
 | 3 |  |  | BLE not implemented | Power failure during flight test | Unable to correctly flash ESCs
 | 2 |  |  |  | Motor control logic not implemented | 
 | 1 |  |  | Application controller sends incorrect GPS waypoints |  | 
 |  | 1 | 2 | 3 | 4 | 5
 | Consequence |  |  |  |  | 
 | No Action
 | Moderate Risk – Take Action
 | High Risk – Seek Immediate remedy

## Slide 23: Mitigation Plan
Risk, by Severity | Mitigation Plan
Unable to correctly flash ESCs | Purchase new ESC hardware with proper firmware
Power failure during flight test | Implementation of low battery voltage flight abort procedure
Motor control logic not implemented | Prioritize task; use manual flight control
BLE not implemented | Prioritize task; use direct flight controller programming
Application controller sends incorrect GPS waypoints | No action required

## Slide 24
Conclusions
Seeking to build a drone to monitor air quality around large chemical fires and explosions.
Finished assembling the frame and soldered all wire connections.
Utilizing two communication protocols UART and I2C which connects to 3 sensors: altitude/pressure sensor, gyroscope, and GPS.
Upcoming goal: Make quadcopter hover with stabilization
Notes: 14:30

## Slide 25
Autonomous Aerial Vehicle
Oct 13th- 2020 | Team 10
Alex Magyari – Team LEAD
Leslie Nix | Ai Nguyen | Sang Nguyen
Project Manager: Dr. Shan

## Slide 26: Project Appendix

## Slide 27: Hardware Construction Diagram
Notes: 5:30

## Slide 28: Drone Performance Calculation
Motion Model Analysis
Notes: 6:30

## Slide 29: Flight Code Specifications
Flight Controller
  Level Flight (< 5 degrees tilt)
  No Steady State Error
Abort Procedures
  Forward Velocity > 10 [m/sec]
  Altitude < 2[m] while not landing
  Position > 15[m] from flight path
  Estimated state deviation > 20%
Data Logging
  Position
  Orientation
  Sensor Output
Notes: 11:00

## Slide 30: Simulation Model
Airframe
  Actuators (Motors)
  Aerodynamics
  6 Degree of Freedom Motions
Environment
  Gravity
  Air Density, Pressure
Sensors
  Conversion of Sensor Output
Notes: 9:00

## Slide 31
PHYSICAL SPECIFICATION AND PERFORMANCE OF DRONE |  |  |  | 
Physical Specification | Frame Dimension | 334 [mm] x 334 [mm] | Propeller | Diameter: 8’’
 |  |  |  | Pitch: 6”
 | Total Weight | 2795 [g] (sensor is attached) | Motors | 34,680 RPM(MAX)
 | Drone Weight | 795 [g] | Microcontroller | MSP432
 | Thrust-to-Weight Ratio | 1.9 | GPS Module | NEO-6M
 | Drone Height | 80 [mm] | BLE Sensor | CC2650
 | Wheelbase | 472 [mm] | Gyroscope Sensor | PMU6500
Performance | Thrust | 5.416 [kg] | Altitude | 122 [m]
 | Maximum Speed | 36 [km/h] | Operation Temperature | 50 to 120 [°F]
 | Operation Distance | Up to 1 [km] | Max Wind Speed | 11 km/h
 | Flight Time | Up to 13 minutes | Battery | Lithium-Ion 6S (22.2V, 1550mAh)
Quadcopter Specifications

## Slide 33: Project Planning and Task Deliberation
Alex directed the team in project planning, where we discussed requirements for each task required to complete each deliverable.
Uploaded the design requirements and priorities into Trello, a list management tool that can be utilized for project planning.

## Slide 34: Flight Control Unit Selection
Processors require minimum 40 General Purpose Input/Output (GPIO) pins
Must be affordable
Processors must have Universal Asynchronous Receiver/ Transmitter (UART) capabilities for communication with external modules
 | TM4C123G | MSP432 | F28379D
GPIO Pins | 40 | 40 | 80
UART | Yes | Yes | Yes
Power Usage | 76-760 [mW] | 2.2-264[mW] | 84-560 [mW]
Cost | $15.33* | $23.59* | $39.87*

## Slide 35: Flight Code

## Slide 36: Flight Controller

## Slide 37: Sensor Processing

## Slide 38: Linear Altitude Tuning Model

## Slide 39: Altitude Nonlinear Response
Before Tuning
After Tuning

## Slide 40: Goal Analysis
Receive GPS coordinates via mobile app
Follow path within 3 [m] margin of error
Forward flight speed of 2-4 [m/sec]
Return to starting points after completing flight

## Slide 41: AUTONOMOUS DRONE - Patent No.: US D760,624 S
Inventor: Antoine Balaresque, Henry W. Bradlow, Robert N. Englin
Assignee: Lily Robotics, Inc., San Farancisco, CA (US)
Claim: The omamental design for an autonomous drone.
Specifications:
  Built-in Camera: Yes
  Mobile App Control: No
  GPS Navigation: No
  Autonomous Flight Control: Yes
  User Interface Control: No
  Bluetooth Communication: No
Team 10’s Drone Specification:
  Built-in Camera: No
  Mobile App Control: Yes
  GPS Navigation: Yes
  Autonomous Flight Control: Yes
  User Interface Control: Yes
  Bluetooth Communication: Yes

## Slide 42: US9891621B2: Control of an unmanned aerial vehicle through multi-touch interactive visualization
Overview of IP
  Methodology for user interaction with unmanned aerial vehicle with portable multifunction device (ie. smart phone)
    Camera and RF-based User Tracking
    Gesture Tracking
    Multi-Touch User Input from Device
  "Follower/Tether"
Comparison to the Current Project
  No direct user modification of flight once set
    Algorithmic determination of flightplan after waypoints selected in software